## Slide 1
Opération XPM
ASTRO
Instabilities in the linear plasma device MISTRAL
A. Escarguel, Y. Camenen, N. Claire, and F. Doveil
PhDs :
C. Rebont (07/2010)
S. Jaeger (10/2010)
T. Lefèvre ( 02/2012)
P. David ( 02/2017)
and post-doc. :
R. Baude (since 2015)

## Slide 2
Opération XPM
ASTRO
MISTRAL
  Toward non-intrusive diagnostics
  Laser Induced Fluorescence (LIF) for ion motion
  Tomography for plasma instabilities
  (Spectro-tomography for Tokamak SOL and cold plasmas
  EFILE : electric field measurement in a plasma)
Dye Laser (LIF)
MISTRAL experiment
Notes: Sondes de Langmuir
Caméras rapides
Diagnostic micro-ondes de n_e
Spectroscopie…

## Slide 3
Opération XPM
ASTRO
Plasma column instabilities in ExB fields:
experimental study in MISTRAL experiment
Notes: Transport « anormal » = non collisionnel
Propulseurs plasma à effet Hall : le transport anormal réduit le confinement des électrons  réduction de l’efficacité du propulseur

## Slide 4
Opération XPM
ASTRO
Plasma instabilities in ExB fields
Plasmas in ExB fields:
Plasma thrusters
Magnetron discharges
Penning gauges…
Charged particles drift in E x B direction.
Interesting when azimuthal drift
 But configuration undermining development of « anomalous » transport of electrons across B (Tokamak fusion problem, favorable in plasma thrusters).
Notes: Transport « anormal » = non collisionnel
Propulseurs plasma à effet Hall : le transport anormal réduit le confinement des électrons  réduction de l’efficacité du propulseur

## Slide 5
Opération XPM
ASTRO
MISTRAL experiment
L = 1.2m
Radius : 4.10-2 m
1.10-4 mbar < PAr < 1.10-2 mbar
B < 25 mT
1 eV < Te < 4 eV
1014 m-3 < Ne < 1016 m-3
Machine built by G. Leclert and Th. Pierre in 2000
Weakly ionized ions  specific instabilities
Presence of ionizing (primary) electrons
Toulouse 21-23 June 2017
Notes: Paramètre Ro star = rayon de Larmor ionique / rayon plasma
E(radial): 100 V/m
significantly influence turbulence characteristics: in usual laboratory devices,
ro* is of the order of 10-1  global modes (large fluctuation, low mode number of the order of unity, weakly developed turbulence) are observed
in large facilities, with ro*~10-3  local modes are observed (large mode number m~100 nonlinearly coupled yielding strong turbulence
DIAGNOSTICS :
Sondes de Langmuir
Caméras rapides
Diagnostic micro-ondes de n_e
Spectroscopie…

## Slide 6
Regular modes rotating around plasma column
[Jaeger POP 2009]
Langmuir probe in the diaphragm shadow : ne.
2 half-cylinders around the column : radial current I.
 Observation of rotating structures (n = a few kHz)
source
probe
½ cylinder
Notes: On peut conserver ces structures pendant 1 ou 2 heures!

## Slide 7
Analytical model for the rotation frequency
of regular modes
Quasi-neutral plasma in diaphragm shadow,
Regular rotation around central plasma : viφ = ω.r,
Ionization neglected in diaphragm shadow,
Ions loose energy through collisions with neutral atoms,
Collisionless electrons,
Cylindrical symetry.
 Simple system:
vS = ver – vir,
ωL = eB/M,
λfi = ion mean free path.
[Annaratone et al. POP 2011]
Notes: Termes convectifs ioniques : les 3 termes en v_ir et r
Termes de friction ions/neutres : les 2 termes en raçine
Terme force B : terme en wL.

## Slide 8
Rotation frequency ν versus magnetic field
o : model
X : exp.

## Slide 9
Rotation frequency versus Pressure
Simple physical model explaining n global behavior
B=100G : + (exp.) ; - (th.)
B=180G : x (exp.) ; -- (th.)
[Annaratone POP 2011]
Notes: Comment se traduit la variation de la fréquence en fct de P ? par la dépendance de lambda_fi inversement proportionelle à n_neutres

## Slide 10
Low frequency instabilities : looking for symetries…
source
column
probes
Flute regular modes
No symetry for « turbulent » plasma
probe

## Slide 11
Low frequency instabilities : Langmuir probes
[Matsukuma et al. Phys. Lett. A 2003]
source
colonne
: measurement plane
Probe measurements
Perturb the plasma (sonification)
Long measuring time > 1 h
Strong hypothesis on symetry
 optical measurements ?
ne probe measurement in a plane ┴ B

## Slide 12
Low frequency instabilities : possible optical measurements…
- : probe polarized at
V > Vplasma
- : photo-diode
(collimated los)
source
los
Photod.
column
probe
Strong correlation between probe and photo-diode signals

## Slide 13
Low frequency instabilities : intensified camera
Caracteristics : Dtmin = 1 ns ; nacq = 25 Hz ; 736x572 pixels
Periodic phenomenon: intensified camera synchronized with probe
Plasma symetry hypothesis
Instabilities in diaphragm shadow : azimutal modes m=1 (1 spiral arm), 2 (2 spiral arms), turbulence
[Escarguel EPJD 2012]
source
camera
column
probe
Notes: m = r x k_teta
Donc, si m=2, alors 2 x lambda_teta = 2 x Pi x r
Donc, on a 2 fois la longueur d’onde azimutale en tournant autour de la colonne centrale.

## Slide 14
Opération XPM
ASTRO
Principle of Laser Induced Fluorescence
Measurement based on :
  Excitation and emission of photons by an atom or an ion. In our case, Ar+ ion.
  Doppler effect.
Fluorescence
460,957nm
LASER
611,492nm
Niveau 1
Niveau 3
Niveau 2,
Level 1 to level 2 transition condition:
Laser frequency = transition 1-2 frequency
Emitted fluorescence proportional to the number of excited ions (atoms)

## Slide 15
Opération XPM
ASTRO
LIF instruments
Dye Laser
Power : 400mW at 611,5nm
Spectral width : 0,5MHz
Multi-Channel Scaler (MCS)
The MCS allows to:
Count photons (detected by a photomultiplier).
Add temporal resolution to measurement.
Usual parameters:
Temporal definition between 5ns et 65535s
Between 4 et 16384 possible temporal channels.
Up to 4 billions repetitions of measurement possible (increase S/B).
Notes: Transport « anormal » = non collisionnel
Propulseurs plasma à effet Hall : le transport anormal réduit le confinement des électrons  réduction de l’efficacité du propulseur

## Slide 16
Opération XPM
ASTRO
LIF on MISTRAL experiment
2 Measurements:
  laser on
  laser off
  Allows to substract background signal (spontaneous emission)
  Synchronization with perturbation to keep temporal definition during recurrences.
Notes: Transport « anormal » = non collisionnel
Propulseurs plasma à effet Hall : le transport anormal réduit le confinement des électrons  réduction de l’efficacité du propulseur

## Slide 17
Opération XPM
ASTRO
Axial velocity distribution function for m=2 mode
No velocity variation. Density fluctuation (~10%) => No drift wave.
Notes: Transport « anormal » = non collisionnel
Propulseurs plasma à effet Hall : le transport anormal réduit le confinement des électrons  réduction de l’efficacité du propulseur

## Slide 18
Opération XPM
ASTRO
Radial and azimuthal measurements
Velocity vector reconstruction in one point
Hypothesis: structure in uniform rotation
  1 = radial velocity
  2 = azimuthal velocity with p/2 phase
  with temporal synchronization of density for the 2 measurements
Probe
1
2
r=3cm
R=5cm, diaphragm
Notes: Transport « anormal » = non collisionnel
Propulseurs plasma à effet Hall : le transport anormal réduit le confinement des électrons  réduction de l’efficacité du propulseur

## Slide 19
LIF measurements in Mistral
- : ion velocity (m/s)
-- : electric field (V/m)
-. : mode m=2 axis
No whole column ExB drift
No clear signature of instability
[Rebont PRL 2011]
Notes: LIF mode m=2
  La vitesse de rotation de la structure (1400m/s) est plus grande que la vitesse de rotation des ions lors de son passage (700m/s).
  Vitesses azimutales des ions lors du passage des bras et des vitesses radiales d’ ́éjection en dehors.
  Fréquence cyclotron ionique = 6kHz – fréq. Rotation = 7,5 kHz (mode m=2) ; 5 khz (mode m=1)

## Slide 20
Tomographic study of magnetized plasma column instabilities (MISTRAL)
P. David PhD thesis
Advantages :
  2D spatial structure of regular modes
  without any hypothesis
  non intrusive
« Turbulent » modes study
Possible « one shot » acquisition
2x64 channels, nacq = 1 MHz
Notes: Etude paramétrique très complète des modes réguliers dans MISTRAL
 La tomographie permet la levé d’ambiguïté sur la structure spatiale des modes

## Slide 21
Mechanical holder
Mechanical holder
Detector
Tomography : experimental set-up
 Instantaneous measurements, or on reproducible phenomenons : spatial structure study of regular modes.

## Slide 22
2 x 64 bundle fibres Ø100 µm x 5 m
128 x SiPM detectors bar
  Gain (> 106, PDE > 30%) with weak voltages/PMTs (∼ 20 to 40 V)
Fast response time : <100 ps
nacq max. = 1 MHz
Limitations :
No spectral resolution
Important noise: “fake“ signals
(after pulse/cross talk)
8x8 matrix detector
Amplification
stage
Captors :
Experimental set-up: captors matrix
Toulouse 21-23 June 2017
Notes: Silicon PhotoMultiplier (SiPM) is an innovative solid state silicon detector with single photon sensitivity. SiPMs are a valid alternative to photomultiplier tubes (PMT detectors)

## Slide 23
Tomography : validation of inversion code

## Slide 24
First tomographic results …
Spatial structures of regular modes
Weak perturbation by probe
Radial profile more peaked: primary electrons
Vp and ne : p/2 phase delay
-40
-40
0
0
40
40
X axis (mm)
Y axis (mm)
Local emissivity of an m=1 flute mode
[P. David POP 2016 ]
Notes: Profil émission tomographie plus piqué que profil radial sonde  les é.p. plus au centre jouent un rôle important dans le rayonnement du plasma

## Slide 25
Spectro-tomography for instabilities study
Study of regular/turbulent structures ?
 diagnostic (ne,Te) Tokamak WEST
Mesurement of nmetastable in a cold plasma
Post-doc. R. Baude (AMIDEX DEMON)
Spectroscopy : spectral resolution
Tomography : spatial resolution
40 lines coupled with CCD / camera
[R. Baude in preparation for RSI]
Toulouse 21-23 June 2017
Notes: Diagnostic plasma de bord WEST
Anomalies spectres plasma He

## Slide 26
Spectro-tomography
Study of a bunch of lines of sight via a single optical access
Opto-mecanical supports
Plasma column
Windows
 400 mm
LoS
Toulouse 21-23 June 2017
Notes: Diagnostic plasma de bord WEST
Anomalies spectres plasma He

## Slide 27
Opération XPM
ASTRO
Development of a diagnostic to measure directly
electric field : EFILE
Electric field  Emission Lyman-α of a probe H (2s) beam
Measurement of static and/or fluctuating electric fields (vacuum or cold plasma, density 1011 cm-3, sheaths) → OK
Project/Challenge :
Measurement of local electric field in Mistral
Measurement of electric field in front of ICRF IShTAR (Ion cyclotron Sheath Test Arrangement) antenna
[Cherigier-Kovacic RSI 2015 ; Doveil PPCF 2016]
Notes: IShTAR : Ondes ICRF → érosion

## Slide 28
  Lamb shift
Lamb-shift due to radiative corrections
ν0
• Second property of hydrogenoids :
Schrödinger’s equation :
Dirac’s equation : fine structure
Radiative corrections :

## Slide 29
  Schematic view of the EFILE experiment
Collection of Lyman α emission
Test chamber: interaction
probe beam – electric field + diagnostics* beam / plasma
Caesium vapor oven (neutralization)
Plasma source : multipolar device
+
Einzel lenses (extraction)
* mass spectrometer, energy analyzer, Langmuir probes

## Slide 30
ASTRO
E measurement in the shadow of a limiter : principle

## Slide 31
Opération XPM
ASTRO
EFILE : results
Diagnostic EFILE in plasma
Diagnostic EFILE in vacuum: comparison with numerical simulation FEM
Formation of a plasma sheath:
Electric field profile measured -in vacuum (white triangle)
-in test plasma (black triangle)

## Slide 32
Opération XPM
ASTRO
Conclusion : MISTRAL experiment
Non-intrusive optical diagnostics:
  LIF measurements
  Tomography/instabilities
  Radiative transfer
  Spectro-tomography ( complex plasmas)
Collaboration with Tokamak WEST :
  AMIDEX DEMON
  Diagnostic (ne, Te) WEST : neutral beam injector test in MISTRAL
  Spectro-tomography
  Neutral beam injector project (TP/CIML/IRFM)  Hélicon
  External collaborations :
  Simulations with code MCC-PIC LAPLACE Toulouse (JP Bœuf)
  Atomic physics : code SOPHIA LULI (F.B. Rosmej)
  New LIA DSC - MHD instabilities PANTA (Japan)
Notes: PANTA : Plasma Assembly for Nonlinear Turbulence Analysis

## Slide 33
Opération XPM
ASTRO
Annexes

## Slide 34
Simon-Hoh instability (Phys. Fluids 1963)
Opération XPM
ASTRO
[Hoh; Simon Phys. Fluids 1963 ; Jaeger PhD 2009 ; Pierre POP 2016]
ExB drift:
Électrons : veq
Friction forces (e-neutrals)
Ions slowed down:
viq < veq
Charge separation: E1
Instability
- Not coherent with LIF
- Universality problem
Notes: Instabilité de SIMON-HOH : profil radial de vitesse inverse au profil de densité

## Slide 36
Radial ions velocity by LIF

[C. Rebont, thèse 2010]

## Slide 37
Mistral diagnostics : Cameras
Ultra-fast camera
max. acq. frequency : 200 kHz
Spatial resolution : 8x8 pixels
Stanford Computer Optics intensified camera
max. acq. frequency: 25 Hz
spatial resolution : 736x572 pixels
min. exposure time : 1 ns
Ultra-fast camera
developped in the lab.

## Slide 38
Relation between plasma radiation and parameters ?
Weak density : coronal model
2 electrons populations : fe = (1 – phot) fcold(Tcold) + phot×fhot(Thot, Ehot)
 Eq. population for an excited state :
 Eq. population for a metastable state:
Notes: Modèle coronal :
  issus des étude de la couronne solaire
  Opposé extrême du modèle ETL pour les plasmas de très hautes densités
  - Probablement pas valable dans MISTRAL pour l’équilibre d’ionisation
2 sets de section efficaces d’excitation par collisions électronique (Bartschat et Yanguas) : résultats similaires

## Slide 39
Coronal model for Argon
Coronal model : B750
Ehot = 40 eV ; Thot = 10 eV ( )
Ehot = 40 eV ; Thot = 20 eV (--)
Ehot = 10 eV ; Thot = 20 eV (o)
 Présence of primary electrons in the shadow of diafragm
 Consistent with energy analyzer maesurements [Jaeger POP 2009]
Experimental :
ne(r = 7,5 cm) = 7,2 x 108 cm-3
Te(r = 7,5 cm) = 2,1 eV
= 3,3 ✕ 10-3 W.m-2.sr-1 (-)
[Escarguel EPJD 2012]
Notes: Collecteur polarisé au potentiel flottant ou négativement : le surplus de charges issues de la chambre source est évacué radialement.

## Slide 40
Measurement with energy analyzer
Notes: Modèle coronal :
  issus des étude de la couronne solaire
  Opposé extrême du modèle ETL pour les plasmas de très hautes densités
  - Probablement pas valable dans MISTRAL pour l’équilibre d’ionisation
2 sets de section efficaces d’excitation par collisions électronique (Bartschat et Yanguas) : résultats similaires

## Slide 41
Large aperture imaging spectrometer
Comparison of the L*Rp product between Czerny Turner and Bowen Chamber spectrometer
B : incoming beam
G : grating
DB : diffracted beam
M1 : primary convex mirror
M2 : secondary concave mirror
C : mirrors curvature centre
F : chamber image focal field
BCS = Bowen Chamber Spectrometer
CTS = Czerny Turner Spectrometer

## Slide 42
Rotation frequency of m=1 mode vs. experiment parameters
ions and electrons momentum conservation (F. Chen 1984) :
Fields
Convective term
Frictions
[Annaratone et al. POP 2011]

## Slide 44: Negative Ion Source for Neutral Beam Injection Plasma rotation in an e-beam sustained magnetized plasma column
0
1
n (1014 m-3)
n (log, 1014 m-3)
f (2.5 V)
Te (5 eV)
ms
t =

## Slide 45
O : brillance exp. ArI(750,4nm)
- : caméra (normalisé)
I (nomr.)
Mode m=1 - Δt = 5 μs – image every 10 μs
Low frequency instabilities : emission spectroscopy
 ArI(750,4 nm) line gives global plasma emission behaviour.

## Slide 46
New configuration
Half-cylinder
Installation of 2 half-cylinders to measure radial current: each half-cylinder can be biased separately.
Notes: 46

## Slide 47
Results
S.Jaeger, et al. (2009)
rotation of 1 arm (mode =1) observed on cylinders
influence of end conditions:
1) grounded collector
=> injected // current = collected current, no radial current
2) floating collector
=> injected // current > collected current => radial current toward cylinders
Increase of cylinder bias  « arm » rotation frequency increase via electric field increase .
Notes: 47

## Slide 48: LIF measurements
Measurement between
r = 0 and 6 cm
DX = 1 cm
Mode frequency: 5 KHz < fci
LIF Dt : 100 ms
150 000 repetitions
Total acquisition time: 2 h for a time-resolved velocity distribution function
Experimental conditions:
  Grounded half-cylinders
  Floating separatrix and collector (-30 V)
  P = 9 10-4 mbar
  B = 16 mT

## Slide 49: Axial distribution function
Modulation of mean axial velocity at the same frequency as perturbation
 possible drift waves

## Slide 50: Radial evolution of velocity
azimuthal
radial
Mean velocity at density maximum
In the ionization zone, almost null velocity at any radius.
No « block » rotation.
Linear evolution of radial velocity
Density/velocity phase
Constant phase close to p/4
Phase: p/2 at center,
0 outside ionization zone

## Slide 51: Results at r=5cm, ionization zone limit
At max and min density ivdf centered at zero velocity.
Non-zero mean radial flux -> no drift wave
azimuthal
Radial velocity always present.
radial
Flux:

## Slide 52: Results at r=5cm
Radial electric field extrema on density fronts  changes sign.
Azimuthal electric field shows:
-max on rising density front
-differences according to used method (change of sign for energy conservation method)

## Slide 53: Conclusion
Axial density modulation measured by LIF
No plasma rigid rotation
No simple ExB drift
No clear instability identification
Study influence of fci
B.M. Annaratone et al., Phys. Plasmas (2011)