## Slide 1
Fluid simulation of instabilities in partially magnetized plasmas
Gerjan Hagelaar
Laboratoire Plasma et Conversion d’Énergie (LAPLACE)
CNRS & Université Paul Sabatier
Toulouse, France

## Slide 2
Introduction
Fluid simulations are widely used in low-temperature plasma research to obtain a qualitative picture of plasma device operation & predict trends
However: not accurate and sometimes qualitatively incorrect
Difficult case: (partially) magnetized low-temperature plasmas (Hall thrusters, Penning discharges, magnetrons, ...) because of plasma instabilities
  very sensitive to fluid approximations
  hard to solve numerically
  large influence on plasma device
Example: anomalous transport in Hall thrusters

## Slide 3
Electron transport in Hall thruster
B
Conductance  Voltage = Current (Ohm's law)
electrons
Along B: large mobility → Boltzmann equilibrium:
Across B: transport by small perpendicular mobility 
300 V
0 V
Electric potential drop in magnetic field barrier to satisfy current continuity:
Field lines are equipotential + diffusion term
G. J. M. Hagelaar et al, J. Appl. Phys. 91, 5592-5598 (2002)

## Slide 4
Problem: anomalous mobility
Measured perpendicular mobility >> classical expression
Add anomalous mobility with fit parameters:
Due to wall collisions and turbulence
Ion energy distributions
Potential + ionization rate
 = 1
K = 0.2
 = 0.2
K = 0.2
J. Bareilles et al, Phys. Plasmas 11, 3035-3046 (2004)

## Slide 5
Anomalous transport due to E×B drift instabilities
J.C. Adam et al, Plasma Phys. Control. Fusion 50, 124041 (2008)
azimuthal
E×B drift
axial
applied E
B
Closed E×B drift in azimuthal direction tends to become unstable and then “leak” across magnetic field barrier
Requires simulation in plane (z,)  B field
PIC simulations: electron-cyclotron drift instability
Also fluid simulations predict drift instabilities & anomalous transport, but with different (unphysical?) behavior – how to handle this?
Azimuthal E-field
PIC simulations (Adam)
Fluid simulations (later this talk)

## Slide 6
applied voltage
ions in phase space
potential
+ plasma density
Transit-time instability in hybrid Hall thruster simulation
J. Bareilles et al, Phys. Plasmas 11, 3035-3046 (2004)
(exceeded by some ion energies)

## Slide 7
Contents of this talk
Purpose: demonstrate that fluid simulations of partially magnetized plasma devices in general involve plasma instabilities (in particular when describing plane B) – and raise questions about how to handle this
Examples from fluid code MAGNIS:
  Magnetic filter in ITER NIS & PEGASES
  Plasma column in CYBELE source
  Hall thruster
Questions:
  Physical relevance, validity, consistency with experiments and PIC simulations?
  Numerical constraints, convergence?

## Slide 8
MAGNIS fluid model @ LAPLACE Toulouse
Multi-fluid: electrons, ions, neutrals
Continuity equations with chemistry source terms
Full momentum equations including inertia terms
Electron energy equation with magnetized heat flux
Quasi-neutrality: plasma potential deduced from current continuity
Boundary conditions from sheath theory, allowing for different wall materials: grounded, biased, dielectric
Evolution in time and 2D plane perpendicular to magnetic field lines
Parallel losses (along field lines) included via effective source terms (2D+½D) allowing for dielectric, grounded, or biased walls
Magnetized fluxes handled through original numerical scheme using prediction/correction on shifted numerical grids

## Slide 9
Main fluid model equations
Continuity & momentum equations for each species :
losses along magnetic field lines included in source term
ionization

## Slide 10
Main fluid model equations
Continuity & momentum equations for each species :
inertia
magnetic force
electric force
collisions
pressure force

## Slide 11
Main fluid model equations
Continuity & momentum equations for each species :
inertia
pressure force
magnetic force
electric force
collisions
electron flux =
parallel to B
very large, no confinement
perpendicular to B
very small
perpendicular to both B and forces
= magnetic drift
Mobility tensor
“drift-diffusion” equation
typically // :  : × = 1000000 : 1 : 1000

## Slide 12
Main fluid model equations
Continuity & momentum equations for each species :

## Slide 13
Main fluid model equations
Continuity & momentum equations for each species :
Quasi-neutrality & current conservation:

## Slide 14
Main fluid model equations
Continuity & momentum equations for each species :
Quasi-neutrality & current conservation:
Electron energy:

## Slide 15
Main fluid model equations
Continuity & momentum equations for each species :
Quasi-neutrality & current conservation:
Electron energy:
Boundary conditions from sheath theory:

## Slide 16
Magnetic filter sources
BATMAN prototype negative ion source for ITER NBI @ IPP Garching
PEGASES thruster @ Ecole Polytechnique
RF heating
Ion extraction grids
B
B
Some (negative) ion sources use a magnetic filter to separate a cold ion extraction region from a hot RF region
E. Speth et al., Nucl. Fusion 46, S220 (2006)
A. Aanesland et al, PSST 23, 044003 (2014)
Difference with EB discharge devices:
Transport driven by pressure rather than applied voltage
Rectangular geometry!

## Slide 17
Closed drift versus bounded drift
B
B
Side view:
Top view:
physical wall
Cylindrical symmetry: magnetic drift forms closed loop  optimal /B2 confinement (if no instabilities)
No cylindrical symmetry: drift bounded by walls  Hall effect: plasma asymmetry & increased 1/B transport across magnetic field barrier
Linear plasma thruster @ University of Michigan
Did not work
Beal and Gallimore AIAA-2001-3649
driving force
driving force

## Slide 18
Hall effect in magnetic filter
Electron flux (m-2s-1)
Plasma density (m-3)
Potential(V)
Electron temperature (eV)
B
12×12×12 cm3 1 mTorr Argon 100 W
15 V
Electron temperature drop across filter due to collisions + poor heat conduction
Hall effect: vertical asymmetry induced by magnetic drift → oblique 1/B electron flux across filter
hot due to RF heating
RF heating
cold because no heating
B
B
0.01 T

## Slide 19
PIC simulations of prototype ITER negative ion source
J. P. Boeuf et al, Phys. Plasmas 19, 113510 (2012)
B
Fully kinetic PIC simulations
Electron current density
Ion current density

## Slide 20
Experimental check of plasma Hall effect
F. Gaboriau, R. Baude, and G. J. M. Hagelaar, Appl. Phys. Lett. 104, 214107 (2014)
Argon, 0.7 Pa, 200 W, 1 mT
Without applied voltage
Applied voltage 10 V
Strong asymmetry of extracted current density profile!

## Slide 21
Fluid instabilities in magnetic filter
Plasma density
Longitudinal, ion acoustic or “transit time” like instability, related to ions becoming supersonic when crossing Te drop
Presence depends on applied V, B, parallel losses, ...
Not observed in PIC simulations or experiments
Almost no drift instabilities, drift stabilized by Hall effect
Instantaneous plasma density (m-3)
Ratio of ion mean velocity to local ion sound speed

## Slide 22
Mesh convergence
6464
Plasma density
(m-3)
Electron temperature (eV)
Ion Mach number
Electric potential
(V)
128128
256256

## Slide 23
Drift instabilities in magnetic filter
Hall effect stabilizes magnetic drift in filter, no anomalous transport issue
Replacing walls by periodic BCs  no Hall effect  small-scale drift instabilities, observed in both PIC and fluid simulations
Plasma density (m-3)
Horizontal E-field (V/m)
Vertical E-field (V/m)
3 cm
Phys. Plasmas 19, 113509 (2012)
periodic boundary
RF heating
B
periodic boundary
Fluid model (with inertia terms)
PIC simulations
  LH  107 rad/s

## Slide 24
Mesh convergence
Plasma density
(m-3)
Electron temperature (eV)
B field (T)
Electric potential
(V)
64128
128256
256512

## Slide 25
Magnetized plasma column
CYBELE negative ion source for NBI under development @ CEA Cadarache
Classical problem: long (cylindrical) plasma column with axial magnetic field, relevant to some low temperature plasma devices (CYBELE, Mistral, Mirabelle, ... )
Plasma sustained by RF heating or filaments located near center
Boundary conditions at ends of column play important role
1.7 mTorr hydrogen
(nT) pressure gradient
(nT)B diamagnetic drift
B
A. Simonin et al, Nucl. Fusion 55, 123020 (2015)

## Slide 26
Rotating instability in plasma column
Successive CCD camera images taken in linear plasma device NAGDIS. From: H. Tanaka et al, Contrib. Plasma Phys. 52 (2012)
Plasma tends to develop one or two "arms" rotating at 2-4×105 rad/s, more or less as rigid objects
13 mT
8 mT
17 mT
B = 3.5 mT

## Slide 27
Plasma parameters in column
Conducting
walls at end of column
Dielectric walls
Current density toward walls at end of column
(Simon short-ciruit)
Time-averaged
radial profiles
Azimuthal profiles in rotating frame
at 2.25×105 rad/s
B = 10 mT
e loss >> i loss
i loss > e loss

## Slide 28
Mesh convergence
Plasma density
(m-3)
Electron temperature (eV)
Electric potential
(V)
3232
6464
128128
256256

## Slide 29
E×B discharge in Hall thruster
Cathode:
injection // B of fixed electron current
Axial size 5 cm
Periodic boundary conditions
Fixed gas density
B
Anode:
sheath model with fixed wall potential
Magnetic field max 170 G
Plume:
full ion absorption, zero local current density
Dielectric walls:
current-free plasma losses // B
Radial size 1.5 cm
Azimuthal size 2.5 cm
Plasma sustainment depends directly on magnetized transport
Transport due to applied voltage rather than pressure gradient
Neutral gas depletion

## Slide 30
Tentative fluid simulation results
Plasma density
(m-3)
Electron temperature (eV)
Ion mean velocity
(m/s)
Ionization source term (m-3s-1)
Electric potential
(V)
Axial
electric field (V/m)
Azimuthal electric field (V/m)
Magnetic field (T)
Gas density
(m-3)

## Slide 31
Problem with mesh convergence
Plasma density
(m-3)
Electron temperature (eV)
Ion mean velocity
(m/s)
Electric potential
(V)
64
128
256

## Slide 32
Tokamak edge plasma
particles
lost // B
2 cm  200 Li
periodic BC
inflow
from tokamak plasma
vessel wall
 small gradient B
B
B = 3 T L// = 20 m H plasma
Scrape-off layer (SOL) = edge of tokamak plasma where magnetic field lines are not closed but terminate at limiter/diverter
While flowing across SOL, plasma is gradually lost by parallel losses
SOL plasma dynamics extensively studied and modeled by fusion plasma community, therefore interesting test case

## Slide 33
Tokamak edge plasma
Very important difference with low temperature plasma (LTP) sources: magnetic field much stronger and nearly constant across SOL → magnetized ions
SOL models based on approximations for small ion Larmor radius e.g.
E×B drift vanishes from current density
dE/dt polarisation drift dominates current conservation
diamagnetic drift
polarization
drift
collision
drift
SOL models cannot describe LTP sources – but LTP models can describe SOL ... provided that ion inertia is taken account, etcetera

## Slide 34
Code comparison: interchange instabilities in SOL
R. Futtersack, PhD thesis, Toulouse, France (2014)
MAGNIS
ion source model, LAPLACE Toulouse
TOKAM2D
SOL model, CEA CAdarache
Constant electon temperature
No vessel wall (spectral method)
Electon energy equation
Sheath BC at vessel wall

## Slide 35
Conclusions & questions
Plasma instabilities pose unavoidable challenges for fluid simulation of partially magnetized plasma devices
Numerical constraints, convergence?
Physical relevance, validity, limitations?
How to patch or improve fluid closures, suppress unphysical artefacts?
Link with basic instability types from literature, dispersion relation?

## Slide 36
Systematic analysis of simple model system
Collaboration with Andrei Smolyakov (& PhD Sarah Sadouni)
Check MAGNIS against analytical linear analysis of basic case E // (nT)  B
No energy equations, fixed T, source term profiles and BCs conditions such that equilibrium solution features constant E, n/n, ve and vi
Inputs: B, E, n/n, Te, Ti, e, i, mi
Fourth order dispersion relation covering many elementary instability types: Simon-Hoh, Farley Buneman, LH, ..., ...
periodic boundary
B
imposed voltage and density drop