## Slide 1: 3D PIC-MCC Model of Hall Thruster
e-mail: francesco.taccogna@cnr.it ExB Plasmas for Space and Industrial Applications – Toulouse 23/06/2017
Francesco Taccogna
Pierpaolo Minelli
P.Las.M.I. research group
Istituto di Nanotecnologia
Consiglio Nazionale delle Ricerche
Bari

## Slide 2: Outline
Critical Points in Hall Thruster
- Evidences from models / experiments
PIC-MCC Model
- Evolution of reduced-dimensional models -> lessons learned
- Modules of PIC-MCC cycle
- Requirements for a 3D representation / Geometrical scaling
Results
- 3D map of electric potential / electron density -> ECD instability
- Electron current density vector plot -> complex transport

## Slide 3
Critical Points - Evidences in HT
Plasma has a strong kinetic behaviour:
low collisionality
pronounced anisotropy
Possible non-classical sheath behavior:
strong secondary electron emission -> material wall dependence
2D sheaths due to azimuthal drift (1D instability is transported along Hall-direction)
Anomalous Electron cross-field transport:
different mechanisms involved; wall-induced, fluctuation-induced, instability-induced, kinetic-induced
how to discern the incidence of each contribution
Strong correlations among the 3 dimensions:
Azimuthal modulation shows axial component
Cathode location
Electron cooling in expansion plume

## Slide 4: Evidences – Electron Energy Probability Function

## Slide 5: Evidences – Electron Current Density Map/Arrow Plot
(Jr2+Jz2)1/2

## Slide 6: Evidences – Inverse Hall Parameter Map

## Slide 7: Fully Kinetic HT Models
Model | Year | Assumptions | Findings
1D(r) - channel | 2006 | - Injection: control number; - Ez; | SEE-instability
2D(r,z) - channel | 2003 |  | acceleration mechanism
2D(r,θ) - channel | 2007 | - Injection: control number; - Ez; | r-θ correlation
3D(r,θ,z) - channel | 2011 | - geometrical scaling | 
3D(x,y,z) - near-field plume | 2013 | - geometrical scaling | 
3D(x,y,z) - channel+NFP | 2015 | - geometrical scaling | 
Balance between consistency and reductionism

## Slide 8: Fully Kinetic HT Models
Model | Year | Assumptions | Findings
1D(r) - channel | 2006 | - Injection: control number; - Ez; | SEE-instability
2D(r,z) - channel | 2003 |  | acceleration mechanism
2D(r,θ) - channel | 2007 | - Injection: control number; - Ez; | r-θ correlation
3D(r,θ,z) - channel | 2011 | - geometrical scaling | 
3D(x,y,z) - near-field plume | 2013 | - geometrical scaling | 
3D(x,y,z) - channel+NFP | 2015 | - geometrical scaling | 

## Slide 9: 3D(r,θ,z) Model
3D(r,θ,z) / discharge channel
- Domain: - radial from inner to outer wall;
- azimuthal: π/2
- axial from anode to exit plane
- Initial condition: start from scratch
- Injection condition: steady-state electron current control method from exit plane
- Field solve: Dielectric surface conductivity neglected
- Electron-atom MCC module
- electron-wall SEE module (Furman-Pivi model)
- Realistic ion mass, vacuum permittivity
- Assumption: - fixed potential (cathode) at the exit plane
- geometrical scaling (f=0.1)
- fixed non-uniform neutral map (no ionization instability)
- Numerical parameter: - Ng=NrxNθxNz=100x128x160 (grid points)
- Np/Ng=30 (particles per cell)
- w=103
- dt=2x10-12 s

## Slide 10: 3D(r,θ,z) Geometrical Scaling
Reduction of size L keeping constant most relevant non-dimensional parameters:
Ionization
Confinement
the discharge still keeps its plasma characteristics:
- S/V changes
- Gradient lenghts scale change
Length | L = f L*
Magnetic field | B = f-1 B*
Neutral density | ng =f-1 ng*
Current | ID = f-2 ID*
(low collisionality)
(global quasi-neutrlity)
(unmagnetized sheath)
(unmagnetized ion)
(gradient driven instability)
(instability growth > ion convection)
f=0.1

## Slide 11: Operative Conditions
Column length | L = 2.5 cm
Internal cylinder radius | Rin = 3.5 cm
External cylinder radius | Rout = 5 cm
Propellant mass flow rate | dm/dt = 4 mg/s
Input power | P = 1350 W
Discharge voltage | Vd = 300 V
Discharge current | Id = 4.5 A
Max radial magnetic field | Br,max = 150 G
SPT-100

## Slide 12: Results – Global Quantities
ANODE
EXIT PLANE
INNER WALL
OUTER WALL
Ie=0.05 A
Ii=0.035 A
Ie=0.022 A
Ise=0.016 A
Ise=0.026 A
Ie=0.032 A

## Slide 13: Results – 3D Electric Potential Map

## Slide 14: Results – 3D Electric Potential Isosurface

## Slide 15: Results – 3D Electron Density Map

## Slide 16: Results – 3D Electron Density Isosurface

## Slide 17: Results – 2D Electron Current Density Map-Arrow Plot
(Jr2+Jz2)1/2 (A/m2)
averaged over q

## Slide 18: Results – 2D Electron Current Density Map
averaged over q

## Slide 19: Results – 2D Electron Current Density Map
averaged over q

## Slide 20: Results – 2D Electron Current Density Map-Arrow Plot
(Jr2+Jq2)1/2 (A/m2)
@ z = 2 mm

## Slide 21: Results – 2D Electron Current Density Map
@ z = 2 mm

## Slide 22: Results – 2D Electron Current Density Map
@ z = 2 mm

## Slide 23: Results – 2D Electric Potential Movie
Dt=20 ns
@ z = 2 mm

## Slide 24: Conclusions
Critical Points in Hall Thruster
- Evidences from models / experiments ->
necessity of kinetic/multidimensional representation
PIC-MCC Model
- Evolution of reduced-dimensional models -> lession learned
- Geometrical scaling
Results
- 3D map of electric potential / electron density -> ECD instability
- Electron current density vector plot -> complex transport
- Indirect influence of the wall on the electron transport